HW#4

(Due October 7)

  - After installing HEC-HMS on your system, open HEC-HMS and choose Tifton Project (if it does not show up by default or otherwise, go to file, and choose ‘open project’). Select the Basin Model item – ‘Tifton’. Click with your right button the green box representing the watershed processes.

  - Now change your “Initial Loss” (i.e., infiltration) to: (a) Green- Ampt; (b) SCS Curve Number method. For (a), assume, initial loss as 0.0 inches and Wetting front suction head as 5.0 inches. Assume, 0% impervious, initial soil moisture content =0.23 and the soil has porosity = 0.50. Run the model for two different saturated hydraulic conductivity – i) Ks = 1.24 mm/hr; and ii) Ks= 0.15 mm/hr. Compare the two discharge hydrographs at the watershed outlet and comment on the differences (explain only qualitatively based on what you’ve learned in class on infiltration).

  - Repeat problem 2, but keeping Ks fixed at 1.24 mm/hr, and assuming that the soil has lower porosity of 0.35. Comment on the difference you observe in the hydrograph simulation.

  - Now change your ‘Initial Loss” to SCS curve number method. Assume initial loss=0.0 inches and 0% impervious. Run the model for Curve Number 55 and 85. Comment on the differences you get in the simulated hydrographs at the basin outlet.